MPC-M25

SECTION XXXXX – CONTROL SYSTEM SPECIFICATION

GENERAL

RELATED DOCUMENTS

Drawings and general provisions of the Contract, including General and Supplementary Conditions and Division 1 Specification Sections, apply to work of this Section.

SUMMARY

This Specification, in conjunction with the Drawings, establishes the requirements necessary to achieve the intended performance, installation and functions of the Media Presentation Controller.

Provide the services necessary to furnish, install, train, and to provide maintenance support for the Media Presentation Controller including all required peripheral apparatus conforming to acceptable industry standards.  All work shall be in accordance with the true intent of these Drawings and Specifications, and as required to leave the Media Presentation Controller complete and in satisfactory operating condition.

Verify dimensions and conditions at the job site prior to installation, and perform installation in accordance with these Specifications, Manufacturers recommendations and the latest edition or revision of all applicable codes and standards.

The Media Presentation Controller shall provide the following features:

Built-in keypad and expansion device ports

Built-in control ports.

Ethernet and e-Control Support.

RoomView and SNMP support.

Built-in keypad, rotary knob and feedback LEDs.

Room Control Processor.

The Media Presentation Controller shall be a scalable device using a proprietary bidirectional communication bus with capability of direct connection, communication and control of other devices including but not limited to the following devices:

Wired touchpanels, LCD keypads, or button keypads

Wireless touchpanels and remotes via RF gateway

Wired HVAC and lighting controllers

Wireless HVAC and lighting controllers via RF gateway

AV signal transmission over UTP systems

AV switchers/processors

Control port expansion modules

CONFLICT BETWEEN DRAWINGS AND SPECIFICATIONS

It is intended that any contractor furnishing materials and/or labor necessary for the completion of this specification shall furnish it in compliance with this specification.  Where conflict exists with other specifications concerning such materials and labor, this specification takes precedence unless otherwise approved in writing by the Engineer.

Drawings pertaining to this specification shall be considered as a part of said specification and shall be a part of the bid documents.

REQIREMENTS OF REGULATORY AGENCIES

The system shall be registered under the most current applicable rulings of the Federal Communications Commission (FCC).  Provide the FCC registration number with the equipment submittal.  All components and installations shall bear an Underwriters' Laboratories (UL) listing and shall conform with the latest edition or revision of the following codes and standards were required:

ANSI - American National Standards Institute

ASTM - American Society for Testing and Materials

BICSI - Building Industry Consulting Services International

EIA - Electronics Industries Association

FCC - Federal Communications Commission

ICEA - Insulated Cable Engineers Association

IEEE - Institute of Electrical and Electronics Engineers

ISO - International Organization for Standardization

NEC - National Electrical Code

NEMA - National Electrical Manufacturer's Association

NFPA - National Fire Protection Association.

TIA - Telecommunications Industry Association

UL - Underwriters Laboratories, Inc.

The code or standard establishing the more stringent requirements shall be followed where areas of conflict occur between codes and standards or between codes and standards and Drawings and Specifications.

SHOP DRAWINGS

Shop Drawings:  Within Seven (7) calendar days after award of contract, submit detailed shop drawings to the Engineer for approval.  Do not begin installation or fabrication without such approval.  All shop drawings shall be marked with the pertaining specification paragraph or drawing number when submitted.

Shop drawings shall be provided clearly depicting any proposed modification to the project drawings.  Any modifications shall be highlighted on the shop drawings.

Shop drawings shall be provided indicating proposed mounting arrangements and details of all equipment, including positioning devices, framework supports and interface with adjacent architecture.

JOB CONDITIONS

Keep the job adequately staffed at all times.  Unless illness, loss of personnel or other circumstances beyond the control of the contractor, maintain the same individual in charge throughout.

Cooperate with all appropriate parties in order to achieve well-coordinated progress with the overall construction completion schedule and satisfactory final results.

Watch for conflicts with work of other contractors on the job and execute, without claim for extra payment, moderate moves or changes as are necessary to accommodate other equipment or to preserve symmetry and aesthetically pleasing appearance.

Immediately report to the Engineer any design or installation irregularities, particularly architectural elements that interfere with the intended coverage angles of loudspeakers and projectors, so that appropriate action may be taken.

Do all cutting, patching and painting necessary for proper and finished installation of the system and repair any damage done as a result of such installation.  Cleanup and dispose of trash from all work areas.

QUALITY ASSURANCE

All materials shall be new and shall conform to applicable provisions of Underwriters Laboratories and the American Standards Association.

Procure and pay for all necessary permits, licenses and inspections and observe any requirements stipulated therein.  Conform in all trades with all local regulations and codes.

Comply with federal, state and local labor regulations and applicable union regulations.

PRODUCTS

MEDIA PRESENTATION CONTROLLER

Provide and install as indicated on the drawing a Media Presentation Controller.

The Media Presentation Controller shall be an integrated controller/interface solution and shall incorporate the following principal devices into a single integrated housing.

Control interface with LED feedback.

Completely programmable and expandable Control Processor.

The Media Presentation Controller shall include a front panel control interface so that the system may be operated directly from the front panel.

The Multimedia Presentation System shall include on the front panel fifteen (15) buttons with LED feedback indicators, one 5-way directional navigation pad, one (1) rotary encoder for programmable scroll or volume control functions and one (1) LED bar graph for volume level or other programmed feedback.

ROOM CONTROL SYSTEM

The Media Presentation Controller shall be an integrated room control processor and control interface. No additional controllers or interfaces shall be required to complete a basic system.

Additional devices including control interfaces, touchpanels, audio and video switchers, amplifiers and volume controllers shall be available from same manufacturer.

Multiple similar or identical systems may be connected and managed via an enterprise level software management suite by same manufacturer.

All room controls shall interface with the Media Presentation Controller as a single unit.  All interface cable for controlled devices shall originate from the Media Presentation Controller.

The Multimedia Presentation Controller shall support multiple communications formats in order to provide complete control of any and all devices connected to the Media Presentation Controller.

The control system shall be of compact design.

Mounting

Requires 3-gang plaster ring or electrical box at least 2.5 inch deep

The control system shall support an RS-485 token passing network bus.

The communications bus shall provide bidirectional communication and power for connected devices.

The communications bus shall support up to 252 proprietary devices simultaneously at distances up to 5000 feet.

Lighting Sensor

The front panel shall include a photo sensor,

Photo sensor shall be programmable for auto-dimming of front panel labeling and other functions.

The Multimedia Presentation Controller shall consist of two principal systems, an internal microprocessor based CPU and external connection ports allowing communication and control of devices connected to the control system.

The microprocessor based CPU shall be configured as follows:

Utilize a real time, event driven, multi-tasking, multi-threaded operating system. Processor shall communicate directly with Ethernet, control ports and proprietary control network utilizing high-speed, parallel bus infrastructure.

Control processor shall utilize a FAT32 file structure.  Support internal communications speed via two, independent communications busses.

First control bus speed shall be at least 40 mb/s,

Second control bus speed shall be at least 300 mb/s.

Control system shall be capable of firing all IR ports simultaneously.

Control System shall support 10/100 BaseT Ethernet Modules, via a direct processor 300 mb/s communications bus that supports all of the following features:

TCP/IP Communications

DHCP and DNS Support

Native Email Client

Remote Diagnostics

Remote Program Loading and Administration

Built-In Web Server

SSL security plug in

PDA Integration and Control, XPanel PDA - Pocket PC 2002

WebTablet Integration and Control – Microsoft Tablet PC

Support user assigned or dynamic IP address.

The control system shall be equipped with the following external connection ports:

Infrared (Output)

4 captive screw terminals comprising two (2) IR or Serial output ports.

IR output up to 1.2 MHz; One-way serial TTL/RS-232 (0-5 Volts) up to 115.2k baud

Input (Digital)

5 captive screw terminals comprising (4) digital or analog input ports (referenced to GND);

Digital Input: Rated for 0-24 Volts DC, input impedance 20k ohms, logic threshold 1.25 Volts DC.

Analog Input: Rated for 0-10 Volts DC, protected to 24 Volts DC maximum, input impedance 20k ohms.

Programmable 5 Volts, 2k ohms pull-up resistor per pin.

Relay

9 captive screw terminals comprising (6) normally open, isolated relays (with shared common).

Rated 1 Amp, 30 Volts AC/DC

MOV arc suppression across contacts

Com

(5) captive screw terminals, comprising a bidirectional RS-232 port.

Up to 115.2k baud; hardware and software handshaking support

(3) captive screw terminals, comprising a bidirectional RS-232 port.

Up to 115.2k baud; software handshaking support

Ethernet

One (1) 8-wire RJ45 with 2 LED indicators.

10/100BaseT Ethernet port.

Green LED indicates link status.

Yellow LED indicates Ethernet activity.

Net

Two (2) sets of (4) captive screw terminals.

Cresnet port and 24 Volt DC power input with parallel pass-thru

Master/Slave selectable

Computer

(1) USB Type B female (behind front cover)

USB 1.1 computer console port

The Multimedia Presentation Controller shall be manufactured by Crestron Electronics, Inc. and shall be a MPC-M25 or engineer approved equal.

EXECUTION

END OF SECTION XXXX